## Slide 1: BLE HCI Command Tester
With python
By Wayne Chiu

## Slide 2: Structure
Serial Driver
Access BT Method
BT Command Tracking
Generate Packet
BT Command data
BT Event data
BT Parameter data
App
Byte Data Display

## Slide 3: File Structure
source -- bt_hci_cmd_test_wc.py
|- dataset -- bt_command.py
|- bt_command_parameter.py
|- bt_error.py
|- bt_event.py
|- bt_event_parameter.py
|- bt_hci_parameter.py
|- bt_packet.py
|- hciresponse.py
|- showlogo.py

## Slide 4: Parameter - [h], [--help]

## Slide 5: Raw reference - Parameters
--raw [RAW_DATA [RAW_DATA ...]] Using command with raw data.
--com COM_PORT COM Port
--baudrate BAUD_RATE Baudrate
--delay DELAY_DURATION Scan event timer
-d, --display Display PDU Data

## Slide 6: Example-Read BD Addr
bt_hci_cmd_test_wc.py --raw 01 09 10 00 -d

## Slide 7: Test Loop Script
ti_schedule_xxtest.bat (outside)
  Parameter %1: initial step first (1: do init, 0: not do)
  Example: (CMD) ti_schedule_xxtest.bat 0
ti_schedule_xxtest.bat (inside)
  Parameter %2: Start Step
    Same as %two_pos%
  Parameter %3: End Step
    Same as % three_pos%

## Slide 8: How to create new test
Create a patch file (*.bat)
Add the Line: (refer ti_readbda.bat)
Update goto section
  :newtest
  if %1a==a goto rbdaddr
Add the raw data and parameter (python) for the new test
  %cmdpath%\bt_hci_cmd_test_wc.py --raw xx xx xx xx…. -d

## Slide 9: How to add test in loop
Update step number (ex. step7)
  if %two_pos% == 7 goto step7
Add Goto section:
  :step7
  Then add the test item shell( *.bat)
Change Step number for last step
  ti_schedule_init.bat 1 1 7 ti_schedule_xxtest
  SET /a three_pos = 7

## Slide 10: How to add command in code -1
Add command string in test_command_set dictionary type.
  bt_hci_cmd_test_wc.py
  Item: test_command_set
  Ex. red word.
For example description
  The first red word: test name which you want to add. (it’s can be any word instead of real command.)
  The second word: it is the PDU format for total raw data. (it only support one command.)
'HCI Inquiry1' : b'\x01\x01\x04\x05\x00\x00\x00\x00\x00', #LAP = 0x9E8B33 Len=0x30

## Slide 11: How to add command in code -2
Use the routine to execute the command you created before.
  hci_command_test_by_inner_string(ser, string)
  The ser is serial port at Host. (ex. com8, etc…)
  The string is your command description you add in test_command_set.

## Slide 12: How to add command in code -3
test_command_set = { ‘this is my Inquiry' : b'\x01\x01\x04\x05\x33\x8B\x9E\x30\x00', #LAP = 0x9E8B33 Len=0x30
…
def main(): global raw_buffer command_for_return_parameter = None parse_args_check() #init... ser = serial.Serial(serial1_port,serial_baudrate,timeout=None, xonxoff=False,rtscts=False,dsrdtr=False) serial_open(ser) hci_command_test_by_inner_string(ser, ' this is my Inquiry') serial_close(ser)

## Slide 13: Q & A

## Slide 14: Next update